| Area Covered: | CUSTOMERS SITES | Assessment Number: | 0002 review no 6 |
| --- | --- | --- | --- |
| Activity Assessed: | JACKING AND BLOCKING TRUCK | Assessor/s: | P . Marlow / E.WOOLLEY |
| Date of Assessment: | Re Assessment no 6 Feb 2021 | Date of Planed Re-Assessment: | Feb 2023 |

| Hazard Identified | Current Controls | Hazard Factor | Risk Factor | Severity Factor | Remedial Action to be Taken | Hazard Factor | Risk Factor | Severity Factor |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Truck sliding off jack while being lifted or lowered | Truck Parked on solid level ground | 50 Medium | 20 Likely | 1000 Medium | Reinforce controls with staff assessments and further training if required | 50 Medium | 5 Possible | 250 Low |
|  | Ensure hand brake is on and chock wheels if required. Correct solid jacking point identified |  |  |  | “ |  |  |  |
|  | Truck raised high enough to let wheels be removed , then blocks placed to support truck, and jack removed |  |  |  | “ |  |  |  |
|  | The practice of raising the truck by tiling the mast while on blocks is now considered unsafe and is forbidden |  |  |  | Method statement revised may 2017 “ |  |  |  |
|  | PPE i.e. safety boots worn |  |  |  | “ |  |  |  |
| Jack failure while truck being lifted or lowered | As above plus | 50 Medium | 5 Possible | 250 Low | Reinforce controls with staff assessments and training. | 50 Medium | 1 Very unlikely | 50 Minimal |
|  | Hands and feet kept clear of truck during operation |  |  |  |  |  |  |  |
|  | All lifting devices visually checked as they are used. |  |  |  |  |  |  |  |
|  | All jacks load tested yearly |  |  |  |  |  |  |  |
|  | Programme of jack inspections |  |  |  |  |  |  |  |
| Failure of blocks while holding truck Failure of blocks while holding truck continued | Standard operation uses TVH nylon interlocking blokes | 50 medium | 5 possible | 250 low |  | 50 medium | 1 very unlikly | minimal50 |
|  | Blocks to be put under flat surfaces of truck where possible |  |  |  | none |  |  |  |
|  | Cracked or damaged blocks to be discarded and replaced ,tvh plastic blocks not to be used on sloping surfaces ie reach trucks |  |  |  |  |  |  |  |
|  | Hands kept away from top of tyre during wheel removal and replacement |  |  |  |  |  |  |  |
|  | Practice of tilting the mast with blocks under it ,to raise the truck has been prohibited On large trucks with 20” tyres use only wooden blocks under the level mast or chassis to support the truck |  |  |  | Risk assessment and method statement reviewed 8/11/16 To be issued to all staff Wooden blocks issued to all fitters |  |  |  |
| Comments: | Signature: |

USE ADDITIONAL SHEETS IF REQUIRED

| HAZARD FACTOR |  | RISK FACTOR |  | SEVERITY FACTOR |
| --- | --- | --- | --- | --- |
| 10 – Minimal 20 – Low 50 – Moderate | 80- High 100 – Very High |  | 1 – Very Unlikely 5 - Possible 20 - Likely | 35 – Probable 50 - Certain |  | 0 – 50 – No Action 51 – 199 – Minimal 200 – 999 - Low | 1000 - 1999 – Medium 2000 – 2999 – High 3000 + Immediate Action Req. |