| Area Covered: | DEPOT/CUSTOMERS SITE | Assessment Number: | 0008 review 6 |
| --- | --- | --- | --- |
| Activity Assessed: | CUTTING OF TYRES WITH GRINDER | Assessor/s: | P.Marlow E WOOLLEY |
| Date of Assessment: | Re assessment 6 Feb 2021 | Date of Planed Re-Assessment: | Feb 2023 |

| Hazard Identified | Current Controls | Hazard Factor | Risk Factor | Severity Factor | Remedial Action Taken | Hazard Factor | Risk Factor | Severity Factor |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cutting disc could shatter or come loose during use. | Safe storage of wheels Wheels used with in date | 80 | 5 | 400 low | Abrasive wheel training carried out 9th febuary 2017 | 80 | 1 | 80 minimal |
| Grinder could slip allowing wheel to contact body | Guard’s not to be removed. Wheel to be chocked while cutting | 80 | 20 | 1600 medium | Abrasive wheel training carried out 9th febuary 2017 | 80 | 5 | 400 low |
| Sparks from grinder could enter eye or ignite material | Eye protection worn at all times Grind so sparks travel away from body. Only use grinder in a secure area free of inflammable material . | 50 | 20 | 1000 medium | Abrasive wheel training carried out 9th February 2017 | 50 | 5 | 100 low |
| Fume from hot rubber could cause breathing problems | Excess rubber to removed with tyre cutter before grinding band. Only cut tyres of as a last resort and always in the open air | 20 | 1 | 20 No action |  | 20 | 1 | 20 No action |
| Comments: | Signature: |

USE ADDITIONAL SHEETS IF REQUIRED

| HAZARD FACTOR |  | RISK FACTOR |  | SEVERITY FACTOR |
| --- | --- | --- | --- | --- |
| 10 – Minimal 20 – Low 50 – Moderate | 80- High 100 – Very High |  | 1 – Very Unlikely 5 - Possible 20 - Likely | 35 – Probable 50 - Certain |  | 0 – 50 – No Action 51 – 199 – Minimal 200 – 999 - Low | 1000 - 1999 – Medium 2000 – 2999 – High 3000 + Immediate Action Req. |